## Slide 1: Harvesting and Working Green Wood
By George Freeman

## Slide 2: Four ways to obtain green wood for turning:
Cut down a tree.

## Slide 3: Four ways to obtain green wood for turning:
Find trees already cut down by other people.

## Slide 4: Four ways to obtain green wood for turning:
Have a friend give you green wood they have obtained.

## Slide 5: Four ways to obtain green wood for turning:
Hang around someone with a sawmill .

## Slide 6: Things to consider about trees
100 foot tall pine tree.
38 inch diameter trunk
2000 board feet of lumber.
20,000 pounds of wet wood.

## Slide 7: Doyle volume chart
Results in board feet of lumber
20 ft. tree/ 24 inch diameter at small end = 500 board feet of lumber
Log length |  | Diameter of log, small end, inside bark (inches) * Results are in board feet per tree (bf) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
6 | feet | 2 | 6 | 14 | 24 | 38 | 54 | 74 | 96 | 122 | 150 | 165 | 198 | 234 | 273 | 315 | 360 | 408 | 459
8 | feet | 2 | 8 | 18 | 32 | 50 | 72 | 98 | 128 | 162 | 200 | 221 | 265 | 313 | 365 | 421 | 481 | 545 | 613
10 | feet | 3 | 10 | 23 | 40 | 63 | 90 | 123 | 160 | 203 | 250 | 276 | 331 | 391 | 456 | 526 | 601 | 681 | 766
12 | feet | 3 | 12 | 27 | 48 | 75 | 108 | 147 | 192 | 243 | 300 | 331 | 397 | 469 | 547 | 631 | 721 | 817 | 919
14 | feet | 4 | 14 | 32 | 56 | 88 | 126 | 172 | 224 | 284 | 350 | 386 | 463 | 547 | 638 | 736 | 841 | 953 | 1,072
16 | feet | 4 | 16 | 36 | 64 | 100 | 144 | 196 | 256 | 324 | 400 | 441 | 529 | 625 | 729 | 841 | 961 | 1,089 | 1,225
18 | feet | 5 | 18 | 41 | 72 | 113 | 162 | 221 | 288 | 365 | 450 | 496 | 595 | 703 | 820 | 946 | 1,081 | 1,225 | 1,378
20 | feet | 5 | 20 | 45 | 80 | 125 | 180 | 245 | 320 | 405 | 500 | 551 | 661 | 781 | 911 | 1,051 | 1,201 | 1,361 | 1,531
22 | feet | 6 | 22 | 50 | 88 | 138 | 198 | 270 | 352 | 446 | 550 | 606 | 727 | 859 | 1,002 | 1,156 | 1,321 | 1,497 | 1,684
24 | feet | 6 | 24 | 54 | 96 | 150 | 216 | 294 | 384 | 486 | 600 | 662 | 794 | 938 | 1,094 | 1,262 | 1,442 | 1,634 | 1,838
26 | feet | 7 | 26 | 59 | 104 | 163 | 234 | 319 | 416 | 527 | 650 | 717 | 860 | 1,016 | 1,185 | 1,367 | 1,562 | 1,770 | 1,991
28 | feet | 7 | 28 | 63 | 112 | 175 | 252 | 343 | 448 | 567 | 700 | 772 | 926 | 1,094 | 1,276 | 1,472 | 1,682 | 1,906 | 2,144
30 | feet | 8 | 30 | 68 | 120 | 188 | 270 | 368 | 480 | 608 | 750 | 827 | 992 | 1,172 | 1,367 | 1,577 | 1,802 | 2,042 | 2,297
32 | feet | 8 | 32 | 72 | 128 | 200 | 288 | 392 | 512 | 648 | 800 | 882 | 1,058 | 1,250 | 1,458 | 1,682 | 1,922 | 2,178 | 2,450
34 | feet | 9 | 34 | 77 | 136 | 213 | 306 | 417 | 544 | 689 | 850 | 937 | 1,124 | 1,328 | 1,549 | 1,787 | 2,042 | 2,314 | 2,603
36 | feet | 9 | 36 | 81 | 144 | 225 | 324 | 441 | 576 | 729 | 900 | 992 | 1,190 | 1,406 | 1,640 | 1,892 | 2,162 | 2,450 | 2,756
38 | feet | 10 | 38 | 86 | 152 | 238 | 342 | 466 | 608 | 770 | 950 | 1,047 | 1,256 | 1,484 | 1,731 | 1,997 | 2,282 | 2,586 | 2,909
40 | feet | 10 | 40 | 90 | 160 | 250 | 360 | 490 | 640 | 810 | 1,000 | 1,103 | 1,323 | 1,563 | 1,823 | 2,103 | 2,403 | 2,723 | 3,063
42 | feet | 11 | 42 | 95 | 168 | 263 | 378 | 515 | 672 | 851 | 1,050 | 1,158 | 1,389 | 1,641 | 1,914 | 2,208 | 2,523 | 2,859 | 3,216
44 | feet | 11 | 44 | 99 | 176 | 275 | 396 | 539 | 704 | 891 | 1,100 | 1,213 | 1,455 | 1,719 | 2,005 | 2,313 | 2,643 | 2,995 | 3,369
46 | feet | 12 | 46 | 104 | 184 | 288 | 414 | 564 | 736 | 932 | 1,150 | 1,268 | 1,521 | 1,797 | 2,096 | 2,418 | 2,763 | 3,131 | 3,522
48 | feet | 12 | 48 | 108 | 192 | 300 | 432 | 588 | 768 | 972 | 1,200 | 1,323 | 1,587 | 1,875 | 2,187 | 2,523 | 2,883 | 3,267 | 3,675
50 | feet | 13 | 50 | 113 | 200 | 313 | 450 | 613 | 800 | 1,013 | 1,250 | 1,378 | 1,653 | 1,953 | 2,278 | 2,628 | 3,003 | 3,403 | 3,828

## Slide 8: Weight Chart based on Doyle Chart
Doyle Log Weight - Hardwoods |  | Table in pounds (lbs.) per log | 
20 ft. tree/ 24 inch diameter at small end = 4,760 lb. of wood
Log length |  | Diameter of log, small end, inside bark (inches) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
6 | feet | 160 | 200 | 260 | 340 | 420 | 560 | 700 | 840 | 1,040 | 1,260 | 1,380 | 1,500 | 1,620 | 1,740 | 1,860 | 1,980 | 2,100 | 2,220
8 | feet | 200 | 260 | 340 | 460 | 600 | 780 | 980 | 1,200 | 1,460 | 1,760 | 1,920 | 2,080 | 2,240 | 2,400 | 2,560 | 2,720 | 2,880 | 3,040
10 | feet | 280 | 320 | 440 | 580 | 780 | 1,000 | 1,260 | 1,560 | 1,880 | 2,260 | 2,460 | 2,660 | 2,860 | 3,060 | 3,260 | 3,460 | 3,660 | 3,860
12 | feet | 320 | 360 | 520 | 720 | 960 | 1,220 | 1,540 | 1,900 | 2,320 | 2,760 | 3,000 | 3,240 | 3,480 | 3,720 | 3,960 | 4,200 | 4,440 | 4,680
14 | feet | 360 | 420 | 600 | 840 | 1,120 | 1,460 | 1,820 | 2,260 | 2,740 | 3,260 | 3,540 | 3,820 | 4,100 | 4,380 | 4,660 | 4,940 | 5,220 | 5,500
16 | feet | 420 | 480 | 700 | 960 | 1,300 | 1,680 | 2,120 | 2,600 | 3,160 | 3,760 | 4,060 | 4,360 | 4,660 | 4,960 | 5,260 | 5,560 | 5,860 | 6,160
18 | feet | 480 | 540 | 800 | 1,080 | 1,480 | 1,900 | 2,420 | 2,940 | 3,580 | 4,260 | 4,560 | 4,860 | 5,160 | 5,460 | 5,760 | 6,060 | 6,360 | 6,660
20 | feet | 540 | 600 | 900 | 1,200 | 1,660 | 2,120 | 2,720 | 3,280 | 4,000 | 4,760 | 5,060 | 5,360 | 5,660 | 5,960 | 6,260 | 6,560 | 6,860 | 7,160
22 | feet | 600 | 660 | 1,000 | 1,320 | 1,840 | 2,340 | 3,020 | 3,620 | 4,420 | 5,260 | 5,560 | 5,860 | 6,160 | 6,460 | 6,760 | 7,060 | 7,360 | 7,660
24 | feet | 660 | 720 | 1,100 | 1,440 | 2,020 | 2,560 | 3,320 | 3,960 | 4,840 | 5,760 | 6,060 | 6,360 | 6,660 | 6,960 | 7,260 | 7,560 | 7,860 | 8,160
26 | feet | 720 | 780 | 1,200 | 1,560 | 2,200 | 2,780 | 3,620 | 4,300 | 5,260 | 6,260 | 6,560 | 6,860 | 7,160 | 7,460 | 7,760 | 8,060 | 8,360 | 8,660
28 | feet | 780 | 840 | 1,300 | 1,680 | 2,380 | 3,000 | 3,920 | 4,640 | 5,680 | 6,760 | 7,060 | 7,360 | 7,660 | 7,960 | 8,260 | 8,560 | 8,860 | 9,160
30 | feet | 840 | 900 | 1,400 | 1,800 | 2,560 | 3,220 | 4,220 | 4,980 | 6,100 | 7,260 | 7,560 | 7,860 | 8,160 | 8,460 | 8,760 | 9,060 | 9,360 | 9,660
32 | feet | 900 | 960 | 1,500 | 1,920 | 2,740 | 3,440 | 4,520 | 5,320 | 6,520 | 7,760 | 8,060 | 8,360 | 8,660 | 8,960 | 9,260 | 9,560 | 9,860 | 10,160
34 | feet | 960 | 1,020 | 1,600 | 2,040 | 2,920 | 3,660 | 4,820 | 5,660 | 6,940 | 8,260 | 8,560 | 8,860 | 9,160 | 9,460 | 9,760 | 10,060 | 10,360 | 10,660
36 | feet | 1,020 | 1,080 | 1,700 | 2,160 | 3,100 | 3,880 | 5,120 | 6,000 | 7,360 | 8,760 | 9,060 | 9,360 | 9,660 | 9,960 | 10,260 | 10,560 | 10,860 | 11,160
38 | feet | 1,080 | 1,140 | 1,800 | 2,280 | 3,280 | 4,100 | 5,420 | 6,340 | 7,780 | 9,260 | 9,560 | 9,860 | 10,160 | 10,460 | 10,760 | 11,060 | 11,360 | 11,660
40 | feet | 1,140 | 1,200 | 1,900 | 2,400 | 3,460 | 4,320 | 5,720 | 6,680 | 8,200 | 9,760 | 10,060 | 10,360 | 10,660 | 10,960 | 11,260 | 11,560 | 11,860 | 12,160
42 | feet | 1,200 | 1,260 | 2,000 | 2,520 | 3,640 | 4,540 | 6,020 | 7,020 | 8,620 | 10,260 | 10,560 | 10,860 | 11,160 | 11,460 | 11,760 | 12,060 | 12,360 | 12,660
44 | feet | 1,260 | 1,320 | 2,100 | 2,640 | 3,820 | 4,760 | 6,320 | 7,360 | 9,040 | 10,760 | 11,060 | 11,360 | 11,660 | 11,960 | 12,260 | 12,560 | 12,860 | 13,160
46 | feet | 1,320 | 1,380 | 2,200 | 2,760 | 4,000 | 4,980 | 6,620 | 7,700 | 9,460 | 11,260 | 11,560 | 11,860 | 12,160 | 12,460 | 12,760 | 13,060 | 13,360 | 13,660
48 | feet | 1,380 | 1,440 | 2,300 | 2,880 | 4,180 | 5,200 | 6,920 | 8,040 | 9,880 | 11,760 | 12,060 | 12,360 | 12,660 | 12,960 | 13,260 | 13,560 | 13,860 | 14,160
50 | feet | 1,440 | 1,500 | 2,400 | 3,000 | 4,360 | 5,420 | 7,220 | 8,380 | 10,300 | 12,260 | 12,560 | 12,860 | 13,160 | 13,460 | 13,760 | 14,060 | 14,360 | 14,660

## Slide 9: Weight of Wood
Wood Species | Fresh Green Wood | Air dried Seasoned Wood | Percentage of loss
 | Density (lb/cf | Density (lb/cf | %
Mesquite | 45 | 43 | 4%
Cedar, Eastern Red | 37 | 33 | 11%
Osage orange | 64 | 57 | 11%
Beech, American | 54 | 45 | 17%
Cherry, black | 45 | 35 | 22%
Honey locust | 58 | 45 | 22%
Pine, Southern Yellow | 53 | 41 | 23%
Ash, Green | 53 | 40 | 25%
Oak, white | 63 | 47 | 25%
Mulberry | 59 | 44 | 25%
Maple, silver | 45 | 33 | 27%
Hickory | 62 | 45 | 27%
Pecan | 62 | 45 | 27%
Hackberry | 51 | 37 | 27%
Maple, Sugar | 59 | 42 | 29%
Post oak | 64 | 45 | 30%
Oak, Red | 61 | 42 | 31%
Walnut, black | 58 | 38 | 34%
Elm, American | 54 | 35 | 35%
Cypress, Southern | 51 | 32 | 37%
Redwood, American | 50 | 28 | 44%
Sycamore | 63 | 34 | 46%

## Slide 10: Transporting turning wood

## Slide 11: Transporting turning wood

## Slide 12: Transporting turning wood

## Slide 13: Felling a tree safely – the tools
Wedges
Plum bobs
Felling sticks
Chainsaws

## Slide 14: Felling a tree safely
Find the center line of the tree in the direction you want it to fall (green line)
Draw a triangle 80% of the width of the tree (yellow line)

## Slide 15
Draw a line horizontal around the rest of the tree staying one to two inches above the bottom of the front triangle (purple line)

## Slide 16: Cut out the front relief wedge

## Slide 17: Start cutting from the back of the tree.
Plunge cut gets between second tree.

## Slide 18: Apply wedges to back of the tree as soon as you have enough room. This keeps the tree from setting back on your saw. This also begins the tilting of the tree in the direction you want it to go.

## Slide 19
Stop the chain saw leaving two inches of wood at the front hinge. Double your wedges and beginning tilting the tree forward as you drive them in.

## Slide 20
Timber! Done right

## Slide 21
Dangers of a rotten core.
Mistakes people make cutting trees:
Cutting the relief cut to deep
Not leaving enough hinge thickness

## Slide 22
Who’s cleaning up the mess of the unwanted wood?

## Slide 23: Where do you take your turning blanks from ???

## Slide 25
4 foot across

## Slide 26: How BIG a piece of wood should you harvest for your turning blanks ???
Rotten limb extending into the core of the tree.

## Slide 27
First Question: What type of turning blank do you want from this tree ???
Second Question: What portion of the tree should you harvest your turning blank from ???

## Slide 28: Processing the wood for storage and turning
200 lbs. of Pecan wood

## Slide 29
Crotch Figure

## Slide 32: Processing the wood for storage and turning

## Slide 33: Processing wood for turning and storage

## Slide 34
The proceding slides dealt with processing green wood for bowl blanks.
How would you process turning blanks for making a round vase ???

## Slide 35: Preparing wood blanks for turning

## Slide 36: Preparing wood blanks for turning
Spalted Pecan
Saving the best Spalted wood

## Slide 37: Preparing wood blanks for a circle turning jig
Find the center
Drill a 3/8” hole
1” deep

## Slide 38: Preparing wood blanks for a circle turning jig
¼” Cap screw with a 3/8” head
3/8” Screw chuck

## Slide 39: Preparing wood blanks for turning

## Slide 40: Spalting green wood in a Fungi Farm to enhance its beauty

## Slide 41: Spalting green wood in a Fungi Farm to enhance its beauty

## Slide 42: Spalting is the beginning stages of fungi attack that will result in rotting of the wood given enough time.
Pecan
Sycamore

## Slide 43: The spalting process needs three things, the decay spores, moisture, and heat. In fresh cut wood, the spores and water are already there. In Texas you have high heat.
Rough turned, green, wet Beech platter coated with Anchor Seal wax will enhance Spalting.

## Slide 44: Spalting green wood in a Fungi Farm to enhance its beauty
Woods that Spalt easily and beautifully
Pecan
Hickory
Sweetgum
Maple
Cherry
Bradford Pear
Beech
Pine
Other light colored woods
Woods that are hard to Spalt or it doesn’t show up in the wood.
Sycamore
Black Walnut
Mesquite
Bois d” Arc
Red Cedar

## Slide 45: Shrinkage and Distortion of green wood
Removal of moisture from the felled tree to levels below the fiber saturation point (about 32% water) causes the wood to shrink.
Pecan
Cherry

## Slide 46: Shrinkage and Distortion of green wood
The water/paper towel example.
The beech wood example.

## Slide 47: Shrinkage and Distortion of green wood
Use a moisture meter to determine the percent of moisture left in green wood.

## Slide 48: Shrinkage and Distortion of green wood
Mesquite
Green Ash

## Slide 49: Shrinkage and Distortion of green wood
Eastern Red Cedar
“Juniperus Virginiana”
Hickory
Different woods shrink at different rates

## Slide 50: Shrinkage and Distortion of green wood
Sweet Gum
Bois d” Arc
Osage Orange
Horse Apple Tree

## Slide 51: Shrinkage and Distortion of green wood
Average shrinkages, |  |  | 
fibre saturation point (FSP)(32%) |  |  | 
to 12% moisture content. |  |  | 
 | Radial | Circumferential | Ratio
Hardwoods | % | % | 
Ash | 4.5 | 7.0 | 1.6
Cherry | 3.5 | 6.5 | 1.9
Elm | 4.5 | 6.5 | 1.4
Holly | 5.0 | 12.0 | 2.4
Sugar Maple | 2.5 | 5.0 | 2.0
White Oak | 3.0 | 5.5 | 1.9
Purple Heart | 2.0 | 4.5 | 2.3
Beech | 3.0 | 6.0 | 2.0
Sycamore | 2.5 | 5.5 | 2.2
Walnut | 2.5 | 3.5 | 1.4
Softwoods |  |  | 
Pine | 2.5 | 4.0 | 1.6

## Slide 52: Shrinkage and Distortion of green wood
Circumferential shrinkage on persimmon wood
Shrinkage of crooked grain Walnut root

## Slide 53: Shrinkage and Distortion of green wood
1. Walnut Root
2. Black Cherry off-cut
3. Beech slab 2” thick
4. Walnut turning blank 2” x 20”

## Slide 54: Shrinkage and Distortion of green wood
Have a saw mill cut your wood into two, three or four inch slabs so it will dry faster. Slabs make great shallow bowls and platters.

## Slide 55: Shrinkage and Distortion of green wood
One of the ways to deal with shrinkage and distortion of your bowl is to rough turn it and leave the walls thick until its dry. Wall thickness should be left 1 to 1 ½” inches

## Slide 56: Shrinkage and Distortion of green wood
Bradford Pear – Which way will it warp and distort during drying?

## Slide 57: Controlling Shrinkage and Distortion
You can control the rate of moisture release by applying coatings to slow down drying of the wood.
Walnut Root with Latex Paint
Black Walnut with Paraffin Wax
Cherry with Anchor Seal

## Slide 58: Controlling Shrinkage and Distortion
Applying anchor seal to slow drying and distortion of wood.

## Slide 59: Controlling Shrinkage and Distortion
A bowl that was allowed to dry to much on the outside, causing stress cracks to open up. Anchor Seal was applied.
As the moisture equalizes through out the bowl the cracks are closing up and the anchor seal is being squeezed out of the cracks.

## Slide 60: Controlling Shrinkage and Distortion
You can remove the water from the wood fibers by immersing in a alcohol bath for 48 hrs. This will help control shrinkage.
Mixed results from this.

## Slide 61: Controlling Shrinkage and Distortion
Microwave drying can speed up drying of a bowl. Must be done slowly and at low heat with repeated cycles.

## Slide 62: Controlling Shrinkage and Distortion
How uncontrolled drying leads to differential drying in different parts of the bowl

## Slide 63: Controlling Shrinkage and Distortion
Wrapping the outside of a bowl or vase slows down the outside drying while allowing the inside to dry faster. This reduces cracking.
Black Walnut Vase
Air Hole

## Slide 64: Controlling Shrinkage and Distortion
Plastic bag used to slow down drying on the bottom of the bowl while allowing the top side to dry quicker.

## Slide 65: Controlling Shrinkage and Distortion
Other methods of relieving stress in wood as
it is drying.
  Steaming wood in a steam chamber will help relieve stress and speed drying.
  Boiling in water relieves stress and speeds drying.

## Slide 66: Dealing with holes, knots, cracks & crooked grain woods
Our repair arsenal

## Slide 67: Dealing with holes, knots, cracks & crooked grain woods
Making wood crack filler using natural wood. Mix with clear epoxy and fill your holes and cracks so they match.

## Slide 68: Dealing with holes, knots, cracks & crooked grain woods
Holes
Filler

## Slide 69: Dealing with holes, knots, cracks & crooked grain woods
Epoxying structural weakness cracks for safety before and during turning.
Walnut
Mesquite

## Slide 70: Dealing with holes, knots, cracks & crooked grain woods
The Red Cedar Vase
1.
4.
3.
2.
5.
6.

## Slide 71: Dealing with holes, knots, cracks & crooked grain woods
Filling the cracks with epoxy
Cracks – inside and out

## Slide 72: Dealing with holes, knots, cracks & crooked grain woods
The Red Cedar Vase

## Slide 73: Dealing with holes, knots, cracks & crooked grain woods

## Slide 74: Dealing with crooked grain woods
Possible methods:
1. Bowl Gouge or other lath tool?
2. Sealing with sanding sealer (shellac) to stiffen the grain.
3. Smoothing with a Card scraper
4. Sanding

## Slide 75: Dealing with crooked grain woods
Heart wood trying to break out of a beech wood bowl.

## Slide 76: Dealing with crooked grain woods
Shrinkage cracking of:
Limb wood
Heart wood or pith

## Slide 77: Dealing with crooked grain woods
A well filled crack
Needs more filling

## Slide 78: Dealing with holes, knots, cracks & crooked grain woods
Walnut Vase
Holes
Cracks

## Slide 79
The End
Thanks to Michael O’Donnell for the use of some of his charts and graphs from his book for this presentation.